## Slide 1: CSCI-1680 DNS
Based partly on lecture notes by Scott Shenker and Rodrigo Fonseca
John Jannotti

## Slide 2
We know how to open TCP connections to a server/port:
  E.g., 128.148.32.110, port 80

## Slide 3: Host names and IP Addresses
IP Addresses
  Numerical address appreciated by routers
  Fixed length, binary numbers
  Hierarchical, related to host location (in the network)
  Examples: 128.148.32.110, 212.58.224.138
Host names
  Mnemonics appreciated by humans
  Variable length, ASCII characters
  Provide little (if any) information about location
  Examples: www.cs.brown.edu, bbc.co.uk

## Slide 4: Separating Naming and Addressing
Names are easier to remember
  www.cnn.com vs 157.166.224.26
Addresses can change underneath
  e.g, renumbering when changing providers
Name could map to multiple addresses
  www.cnn.com maps to at least 6 ip addresses
  Enables
    Load balancing
    Latency reduction
    Tailoring request based on requester’s location/device/identity
Multiple names for the same address
  Aliases: www.cs.brown.edu and cs.brown.edu
  Multiple servers in the same node (e.g., apache virtual servers)

## Slide 5: Scalable Address <-> Name Mappings
Originally kept in a local file, hosts.txt
  Flat namespace
  Central administrator kept master copy (for the Internet)
  To add a host, emailed admin
  Downloaded file regularly
Completely impractical today
  File would be huge (gigabytes)
  Traffic implosion (lookups and updates)
    Some names change mappings every few days (dynamic IP)
  Single point of failure
  Impractical politics (security, ownership, etc…)

## Slide 6: Goals for an Internet-scale name system
Scalability
  Must handle a huge number of records
    With some software synthesizing names on the fly
  Must sustain update and lookup load
Distributed Control
  Let people control their own names
Fault Tolerance
  Minimize lookup failures in face of other network problems

## Slide 7: The good news
Properties that make these goals easier to achieve
  Read-mostly database
    Lookups MUCH more frequent than updates
  Loose consistency
    When adding a machine, not end of the world if it takes minutes or hours to propagate
These suggest aggressive caching
  Once you’ve lookup up a hostname, remember
  Don’t have to look again in the near future

## Slide 8: Domain Name System (DNS)
Hierarchical namespace broken into zones
  root (.), edu., brown.edu., cs.brown.edu.,
  Zones separately administered :: delegation
  Parent zone tells you how to find servers for subdomains
Each zone served from multiple replicated servers

## Slide 9: DNS Architecture
Hierarchy of DNS servers
  Root servers
  Top-level domain (TLD) servers
  Authoritative DNS servers
Performing the translation
  Local DNS servers
  Resolver software

## Slide 10: Resolver operation
Apps make recursive queries to local DNS server (1)
  Ask server to get answer for you
Server makes iterative queries to remote servers (2,4,6)
  Ask servers who to ask next
  Cache results aggressively

## Slide 11: DNS Root Server
Located in Virginia, USA
How do we make the root scale?
Verisign, Dulles, VA

## Slide 12: DNS Root Servers
13 Root Servers (www.root-servers.org)
  Labeled A through M (e.g, A.ROOT-SERVERS.NET)
Does this scale?
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium
Palo Alto, CA
I Autonomica, Stockholm
K RIPE London
M WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign

## Slide 13: DNS Root Servers
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium,
Palo Alto, CA
(and 37 other locations)
I Autonomica, Stockholm (plus 29 other locations)
K RIPE London (plus 16 other locations)
M WIDE Tokyo
plus Seoul, Paris, San Francisco
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles, NY, Chicago)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign (21 locations)
13 Root Servers (www.root-servers.org)
  Labeled A through M (e.g, A.ROOT-SERVERS.NET)
Replication via anycasting

## Slide 14: TLD and Authoritative DNS Servers
Top Level Domain (TLD) servers
  Generic domains (e.g., com, org, edu)
  Country domains (e.g., uk, br, tv, in, ly)
  Special domains (e.g., arpa)
  Typically managed professionally
Authoritative DNS servers
  Provides public records for hosts at an organization
    e.g, for the organization’s own servers (www, mail, etc)
  Can be maintained locally or by a service provider

## Slide 15: DNS Caching
All these queries take a long time!
  And could impose tremendous load on root servers
  This latency happens before any real communication, such as downloading your web page
Caching greatly reduces overhead
  Top level servers very rarely change
  Popular sites visited often
  Local DNS server caches information from many users
How long do you store a cached response?
  Original server tells you: TTL entry
  Server deletes entry after TTL expires

## Slide 16: Negative Caching
Remember things that don’t work
  Misspellings like www.cnn.comm, ww.cnn.com
These can take a long time to fail the first time
  Good to cache negative results so it will fail faster next time
But negative caching is optional, and not widely implemented
  TTL is tricky. Maybe the reason you’re asking for a non-existent host is because you expect it to exist soon.

## Slide 17: Reverse Mapping
How do we get the other direction, IP address to name?
Addresses have a natural hierarchy:
  128.148.34.7
But, most significant element comes first
Idea: reverse the numbers: 7.34.148.128 …
  and look that up in DNS
Under what TLD?
  Convention: in-addr.arpa
  Lookup 7.34.148.128.in-addr.arpa
  in6.arpa for IPv6

## Slide 18: DNS Protocol
TCP/UDP port 53
Most traffic uses UDP
  Lightweight protocol has 512 byte message limit
  Retry using TCP if UDP fails (e.g., reply truncated)
TCP requires messages boundaries
  Prefix all messages with 16-bit length
Bit in query determines if query is recursive

## Slide 19: Resource Records
All DNS info represented as resource records (RR)
name [ttl] [class] type rdata
  name: domain name
  TTL: time to live in seconds
  class: for extensibility, normally IN (1) “Internet”
  type: type of the record
  rdata: resource data dependent on the type
Two important RR types
  A – Internet Address (IPv4)
  NS – name server
Example RRs
  www.cs.brown.edu. 86400 IN A 128.148.32.110
  cs.brown.edu. 86400 IN NS dns.cs.brown.edu.
  cs.brown.edu. 86400 IN NS ns1.ucsb.edu.

## Slide 20: Some important details
How do local servers find root servers?
  DNS lookup on a.root-servers.net ?
  Servers configured with root cache file
  Contains root name servers and their addresses
  . 3600000 IN NS A.ROOT-SERVERS.NET.
  A.ROOT-SERVERS.NET. 3600000 A 198.41.0.4
  ...
How do you get addresses of other name servers?
  To obtain the address of www.cs.brown.edu, ask a.edu-servers.net, says a.root-servers.net
  How do you find a.edu-servers.net?
  Glue records: A records in parent zone

## Slide 21: Example
dig . ns
dig +norec www.cs.brown.edu @a.root-servers.net
dig +norec www.cs.brown.edu @a.edu-servers.net
dig +norec www.cs.brown.edu @bru-ns1.brown.edu
www.cs.brown.edu. 86400 IN A 128.148.32.12

## Slide 22: Structure of a DNS Message
Same format for queries and replies
  Query has 0 RRs in Answer/Authority/Additional
  Reply includes question, plus has RRs
Authority allows for delegation
Additional for glue, other RRs client might need

## Slide 23: Header format
Id: match response to query; QR: 0 query/1 response
RCODE: error code.
AA: authoritative answer, TC: truncated,
RD: recursion desired, RA: recursion available

## Slide 24: Other RR Types
CNAME (canonical name): specifies an alias
www.google.com. 446199 IN CNAME www.l.google.com.
www.l.google.com. 300 IN A 72.14.204.147
MX record: specifies servers to handle mail for a domain (the part after the @ in email addr)
  Different for historical reasons
SOA (start of authority)
  Information about a DNS zone and the server responsible for the zone
PTR (reverse lookup)
7.34.148.128.in-addr.arpa. 86400 IN PTR quanto.cs.brown.edu.

## Slide 25: Reliability
Answers may contain several alternate servers
Try alternate servers on timeout
  Exponential backoff when retrying same server
Use same identifier for all queries
  Don’t care which server responds, take first answer

## Slide 26: Inserting a Record in DNS
Your new startup helpme.com
Get a block of addresses from ISP
  Say 212.44.9.128/25
Register helpme.com at GoDaddy.com (for ex.)
  Provide name and address of your authoritative name server (primary and secondary)
  Registrar inserts RR pair into the com TLD server:
    helpme.com NS dns1.helpme.com
    dns1.helpme.com A 212.44.9.129
Configure your authoritative server (dns1.helpme.com)
  Type A record for www.helpme.com
  Type MX record for foobar.com

## Slide 27: Inserting a Record in DNS, cont
Need to provide reverse PTR bindings
  E.g., 212.44.9.129 -> dns1.helpme.com
Normally, these would go into the 9.44.212.in-addr.arpa zone
Problem: you can’t run the name server for that domain. Why not?
  Your block is 212.44.9.128/25, not 212.44.9.0/24
  Whoever has 212.44.9.0/25 wouldn’t be happy with you setting their PTR records
Solution: [RFC2317, Classless Delegation]
  Install CNAME records in parent zone, e.g:
  129.9.44.212.in-addr.arpa CNAME 129.ptr.helpme.com

## Slide 28: DNS Measurements (Data from MIT, 2000: http://nms.lcs.mit.edu/papers/dns-ton2002.pdf)
What was being looked up?
  60% A, 25% PTR, 5% MX, 6% ANY
Latency
  Median ~100ms (90th percentile ~500ms)
Query packets per lookup: ~2.4
Top 10% of domains  ~70% of lookups
  Great for caching!
9% of lookups are unique
  Caching can’t hit more than 91%
Cache hit rates actually ~75%

## Slide 29: DNS Measurements (Data from MIT, 2000)
Does DNS give back answers?
  ~23% of queries do not elicit an answer
  ~13% return NXDOMAIN (or similar)
    Mostly reverse lookups
  Only ~64% of queries are successful
~63% of DNS packets in unanswered queries
  Failing queries are frequently retransmitted
  99.9% successful queries have <= 2 retransmissions

## Slide 30: DNS Security
You go to starbucks, how does your browser find www.google.com?
  Ask local name server, obtained from DHCP
  You implicitly trust this server
  Can return any answer for google.com, including a malicious IP that poses as a man in the middle
How can you know you are getting correct data?
  Today, you can’t for all sources
  HTTPS can help
  DNSSEC extension allow you to verify

## Slide 31: DNS Security 2 – Cache Poisoning
Suppose you control evil.com. You receive a query for www.evil.com and reply:
;; QUESTION SECTION:
;www.evil.com. IN A
;; ANSWER SECTION:
www.evil.com. 300 IN A 212.44.9.144
;; AUTHORITY SECTION:
evil.com. 600 IN NS dns1.evil.com.
evil.com. 600 IN NS google.com.
;; ADDITIONAL SECTION:
google.com. 10000 IN A 212.44.9.155
Glue record pointing to your IP, not Google’s
Gets cached!

## Slide 32: Cache Poisoning # 2
But how do you get a victim to look up evil.com?
You might connect to their mail server and send
  HELO www.evil.com
  Which their mail server then looks up to see if it corresponds to your IP address (SPAM filtering)
Mitigation (bailiwick checking)
  Only accept glue records from the domain you asked for

## Slide 33: Cache Poisoning
Another possibility: bad guy at Starbucks, can sniff or guess the ID field the local server will use
  Not hard if DNS server generates ID numbers sequentially
  Can be done if you force the DNS server to look up something in your name server
  Guessing has 1 in 65535 chance (Or does it?)
Now:
  Ask the local server to lookup google.com
  Spoof the response from google.com using the correct ID
  Bogus response arrives before legit one (maybe)
Local server caches first response it receives
  Attacker can set a long TTL
Notes: Can send multiple responses almost at the same time.

## Slide 34: Kaminsky Exploit
If good guy wins the race, you have to wait until the TTL to race again
But…
  What if you start a new race, for AAAA.google.com, AAAB.google.com, …?
  Forge CNAME responses for each
  Circumvents bailiwick checking

## Slide 35: Countermeasures
Randomize id
  Used to be sequential
Randomize source port number
  Used to be the same for all requests from the server
Offers some protection, but attack still possible

## Slide 36: Solution: signatures
Signature: cryptographic way to prove a party is who they say they are
Requires a chain of trust
DNSSEC deployment is underway

## Slide 37: Great Firewall of China
Inject false responses to DNS queries passing through Chinese AS’es!
The Collateral Damage of Internet Censorship by DNS Injection. Sigcomm CCR 42, 3 (June 2012)

## Slide 38: Backup Slides
Good information, but not covered in class

## Slide 39: Some more DNS fun
You can use DNS to tunnel data!
Steps:
  Start up a Name Server for a domain you control
  Send info encoding data in the domain name part of a query
  Server encodes response in a TXT record
Why? DNS is often not blocked in airports, etc
This has been a final project in this class!

## Slide 40: SOPA - H. R. 3261 October 2011
“A BILL To promote prosperity, creativity, entrepreneurship, and innovation by combating the theft of U.S. property, and for other purposes”
…
A service provider shall take technically feasible and reasonable measures designed to prevent access by its subscribers located within the United States to the foreign infringing site (or portion thereof) that is subject to the order, including measures designed to prevent the domain name of the foreign infringing site (or portion thereof) from resolving to that domain name’s Internet Protocol address.
Would this work?
102.c.2

## Slide 41: SOPA
Provider filtering would interact badly with DNSSEC
Filtering would be easy to circumvent
  Circumvention could expose users to malicious DNS servers
Could cause collateral damage
  E.g., blog1.blogspot.com vs blog2.blogspot.com
The bill was withdrawn in 2012 after major online outcry, but highlights the importance of understanding technical underpinnings.
See http://www.circleid.com/pdf/PROTECT-IP-Technical-Whitepaper-Final.pdf for details