## Slide 1: CSCI-1680 Physical Layer Link Layer I
Based partly on lecture notes by David Mazières, Phil Levis, John Jannotti
Rodrigo Fonseca

## Slide 2: Today
Physical Layer
  Modulation and Channel Capacity
  Encoding
Link Layer I
  Framing

## Slide 3: Layers, Services, Protocols
Network
Link
Physical
Transport
Application
Service: move bits to other node across link
Service: move frames to other node across link.
May add reliability, medium access control
Service: move packets to any other node in the network
IP: Unreliable, best-effort service model
Service: multiplexing applications
Reliable byte stream to other node (TCP),
Unreliable datagram (UDP)
Service: user-facing application.
Application-defined messages

## Slide 4: Physical Layer (Layer 1)
Responsible for specifying the physical medium
  Type of cable, fiber, wireless frequency
Responsible for specifying the signal (modulation)
  Transmitter varies something (amplitude, frequency, phase)
  Receiver samples, recovers signal
Responsible for specifying the bits (encoding)
  Bits above physical layer -> chips

## Slide 5: Modulation
Specifies mapping between digital signal and some variation in analog signal
Why not just a square wave (1v=1; 0v=0)?
  Not square when bandwidth limited
Bandwidth – frequencies that a channel propagates well
  Signals consist of many frequency components
  Attenuation and delay frequency-dependent

## Slide 6: Components of a Square Wave
Graphs from Dr. David Alciatore, Colorado State University

## Slide 7: Approximation of a Square Wave
Graphs from Dr. David Alciatore, Colorado State University

## Slide 8: Idea: Use Carriers
Only use frequencies that transmit well
Modulate the signal to encode bits
OOK: On-Off Keying
ASK: Amplitude Shift Keying

## Slide 9: Idea: Use Carriers
Only use frequencies that transmit well
Modulate the signal to encode bits
FSK: Frequency Shift Keying
PSK: Phase Shift Keying

## Slide 10: How Fast Can You Send?
Encode information in some varying characteristic of the signal.
If B is the maximum frequency of the signal
C = 2B bits/s
(Nyquist, 1928)
Notes: Intuition: 2B comes from Nyquist’s

## Slide 11: Can we do better?
So we can only change 2B/second, what if we encode more bits per sample?
  Baud is the frequency of changes to the physical channel
  Not the same thing as bits!
Suppose channel passes 1KHz to 2KHz
  1 bit per sample: alternate between 1KHz and 2KHz
  2 bits per sample: send one of 1, 1.33, 1.66, or 2KHz
  Or send at different amplitudes: A/4, A/2, 3A/4, A
  n bits: choose among 2n frequencies!
What is the capacity if you can distinguish M levels?

## Slide 12: Example
Phase
Amplitude
Notes: Used for some forms of digital TV

## Slide 13: Hartley’s Law
C = 2B log2(M) bits/s
Great. By increasing M, we can have as large a capacity as we want!
Or can we?

## Slide 14: The channel is noisy!

## Slide 15: The channel is noisy!
Noise prevents you from increasing M arbitrarily!
This depends on the signal/noise ratio (S/N)
Shannon: C = B log2(1 + S/N)
  C is the channel capacity in bits/second
  B is the bandwidth of the channel in Hz
  S and N are average signal and noise power
  Signal-to-noise ratio is measured in dB = 10log10(S/N)

## Slide 16: Putting it all together
Noise limits M!
2B log2(M) ≤ B log2(1 + S/N)
M ≤ √1+S/N
Example: Telephone Line
  3KHz b/w, 30dB S/N = 10ˆ(30/10) = 1000
  C = 3KHz log2(1001) ≈ 30Kbps

## Slide 17: Encoding
Now assume that we can somehow modulate a signal: receiver can decode our binary stream
How do we encode binary data onto signals?
One approach: 1 as high, 0 as low!
  Called Non-return to Zero (NRZ)
0
0
1
0
1
0
1
1
0
NRZ
(non-return to zero)
Clock
Notes: Low is not necessarily 0V, (or rest), could be -1, for example; hence the name.
Assume we can change the value once per clock cycle.

## Slide 18: Drawbacks of NRZ
No signal could be interpreted as 0 (or vice-versa)
Consecutive 1s or 0s are problematic
Baseline wander problem
  How do you set the threshold?
  Could compare to average, but average may drift
Clock recovery problem
  For long runs of no change, could miscount periods

## Slide 19: Alternative Encodings
Non-return to Zero Inverted (NRZI)
  Encode 1 with transition from current signal
  Encode 0 by staying at the same level
  At least solve problem of consecutive 1s
0
0
1
0
1
0
1
1
0
Clock
NRZI
(non-return to zero
intverted)

## Slide 20: Manchester
Map 0  chips 01; 1  chips 10
  Transmission rate now 1 bit per two clock cycles
Solves clock recovery, baseline wander
But cuts transmission rate in half
0
0
1
0
1
0
1
1
0
Clock
Manchester
Notes: 50% efficiency

## Slide 21: 4B/5B
Can we have a more efficient encoding?
Every 4 bits encoded as 5 chips
Need 16 5-bit codes:
  selected to have no more than one leading 0 and no more than two trailing 0s
  Never get more than 3 consecutive 0s
Transmit chips using NRZI
Other codes used for other purposes
  E.g., 11111: line idle; 00100: halt
Achieves 80% efficiency

## Slide 22: 4B/5B Table

## Slide 23: Encoding Goals
DC Balancing (same number of 0 and 1 chips)
Clock synchronization
Can recover some chip errors
Constrain analog signal patterns to make signal more robust
Want near channel capacity with negligible errors
  Shannon says it’s possible, doesn’t tell us how
  Codes can get computationally expensive
In practice
  More complex encoding: fewer bps, more robust
  Less complex encoding: more bps, less robust

## Slide 24: Last Example: 802.15.4
Standard for low-power, low-rate wireless PANs
  Must tolerate high chip error rates
Uses a 4B/32B bit-to-chip encoding

## Slide 25: Questions?
Photo: Lewis Hine

## Slide 26: Next Week
Next class: link layer
Thursday: HW1 out