## Slide 1: CSCI-1680 Wrap-up Lecture
Rodrigo Fonseca
With some material from Jen Rexford

## Slide 2: Administrivia
Today is the last class!
Two (to four) things to go:
  Final project, due Dec 11th
  Final Exam: Saturday, Dec 20th, 2PM-4PM, CIT 165
  Optional: HW4, follow-up on HW0, bonus points
  Capstone: either addition to project 4 OR LT Project

## Slide 3: How do you study?
  Any covered topic is fair game, but more emphasis on content given after midterm (TCP on)
  Lecture slides, homeworks, plus relevant sections of the book
  Past homework and exam questions
    Fall 2013
    Fall 2012
    Spring 2012
    Spring 2011
  If in doubt, topics not covered in class will not be on the exam (even if on slides)

## Slide 4: What you (hopefully) learned from this course
Skill: Network programming
  C programming (some of you)
  Socket programming
  Server programming
  Implementing protocols
Knowledge: How the Internet Works
  IP Protocol suite
  Internet Architecture
  Applications (Web, DNS, P2P, …)
Insight: key concepts
  Protocols
  Layering
  Naming

## Slide 5: Today
Cut across protocols, identify principles
Internet Architecture
  Virtues and challenges going forward!

## Slide 6: Networking Principles
We saw many layers and protocols, but some principles are common to many
Some are general CS concepts
  Hierarchy
  Indirection
  Caching
  Randomization
Some are somewhat networking-specific
  Layering
  Multiplexing
  End-to-end argument
  Soft-state

## Slide 7: Layering
Strong form of encapsulation, abstraction
Each layer has three interfaces:
  Services provided to upper layer
  Protocol to communicate with peer at the same layer
  Using the services of the lower layer
Provided interface hides all details of internal interface and lower layers
Can be highly recursive
  E.g., IP over DNS, File system over Gmail!

## Slide 8: Layering on the Internet
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 9: Layering: IP as a Narrow Waist
Many applications protocols on top of UDP & TCP
IP works over many types of networks
This is the “Hourglass” architecture of the Internet.
  If every network supports IP, applications run over many different networks (e.g., cellular network)

## Slide 10: Layering: Data Encapsulation
One layer’s data is the (opaque) payload of the next
  Stream (Application)
  Segments (TCP)
  Packets (IP)
  Frames (Ethernet)
  Encoding: bits -> chips
  Modulation: chips -> signal variations
Ethernet Frame
IP Packet
TCP Segment
Application data

## Slide 11: Protocols
Specifications for communication
  Data formats
  Behaviors (FSMs)
Allow
  Interoperability
  Independent implementations
  Don’t need to specify everything
    E.g., TCP Congestion Control
Postel’s Robustness Principle
  "Be liberal in what you accept, and conservative in what you send” (RFC 1122)
Notes: How does this principle show up, for example, in web browsers?
Other examples?

## Slide 12: Multiplexing
Multiple streams/flows can share at different levels
  Important to be able to de-multiplex: need naming
Sharing
  Cost: infrastructure sharing
  Access: single channel sharing
  Reuse: Implementation sharing
Notes: How do you demultiplex different protocols on top of Ethernet?
different packet flows on Ethernet?
different transport protocols on IP?
different flows on TCP?
different http servers on the same IP address?

## Slide 13: Multiplexing: Cost
Multiple flows/streams can share a link/path
  Packet switching
  Circuit switching
Issues
  Coordinate access
    In time, in space, in frequency
  De-multiplexing (name, id)

## Slide 14: Multiplexing: Access
Sharing a single channel
E.g.,
  NAT: multiple nodes share a single IP address
    De-multiplexing: NAT uses 5-tuple to disambiguate
  SSH port forwarding
    Only port 22 is open, can tunnel other ports
    ssh other.host.com –L 5900:other.host.com:5900
  VPN

## Slide 15: Multiplexing: Reuse
No need to re-implement functionality
  Several streams/flows can use the services of a protocol
E.g.:
  IP/ARP/AppleTalk on Ethernet: demux EtherType
  TCP/UDP/DCCP/… on IP: demux Protocol ID
  HTTP/SIP/SMTP/… on TCP/UDP: demux on Port
  Multiple hosts on one HTTP server: demux on Host: field

## Slide 16: End-to-End Argument
“The end knows best”
“The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible. (Sometimes an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)”
End-to-end arguments in system design. Saltzer, Reed, and Clark. Technology (100), 1984

## Slide 17: End-to-end argument
Reliability:
  File transfer application: even through TCP, has to check for file correctness (e.g., BitTorrent hashes)
  So reliability by the transport layer is redundant
  Would work even on top of UDP
Multihop wireless:
  10 hops, 10% chance of packet loss per hop:
  Chance of success: 0.910 ~ 35%
  If you do up to 3 retransmissions per hop, loss drops to 0.13 = 0.001 per hop => chance of success 0.99910 ~ 99% !
    But can’t make it 0 => still require end-to-end check!
Notes: To see this: what is the chance of a packet arriving successfully? 0.9 & 0.9 & … 0.9
If you do retransmissions, what is the chance of a packet NOT making it through a link? 0.1^3 = 0.001
Now, 0.999^10 = 99%!

## Slide 18: End-to-end argument: examples
Encryption: need assurance of no tampering, can only prove if the end point encrypted the message
  Doesn’t matter if the network automatically encrypts
Duplicate suppression
  “Don’t click submit twice”: even though TCP is underneath, two requests will be different data for the network, application must enforce at-most-once
Automatic recovery
  Airline reservation: rather than guaranteeing that every request can survive system crashes, rely on operators to retry.

## Slide 19: End-to-end argument
Instinctively we like modularity and clean interfaces
  Which means putting functionality in low-level abstractions
Examples: reliability, in-order delivery, security
But some applications won’t be able to rely on this
  Low level functionality might be redundant
  Or might be insufficient
  Or might be useless for some applications
  Or might be harmful – e.g., real-time audio over a reliable, in-order delivery channel
Use as a guiding principle or where to place functionality

## Slide 20: Hierarchy
Scalability of large systems
  Cannot store all information everywhere
  Cannot centrally control every component
Hierarchy as a way to manage scale
  Divide large system in smaller pieces
  Summarize information about each piece
Hierarchy as a way to divide control
  Decentralized management of pieces
Many examples of hierarchy in the Internet

## Slide 21: Hierarchy Examples: IP Routing
IP Addressing
  Hierarchical assignment of address blocks
  IANA -> Regional Internet Registries -> ISPs
  Decentralized control
Topology
  (Roughly) correlated with addressing
  Allows aggregation (CIDR)
    Brown owns 128.148.0.0/16
  Decreases size of routing tables!

## Slide 22: Hierarchy Examples: IP Routing
AS-level Topology
  Separates intra and inter-domain routing
  ASs have own economic interests
  Delegation of control
    Policy in inter-domain routing
    Complete control of intra-domain routing
Hierarchical Topology
  Transit, Multi-homed, Stub ASs

## Slide 23: Hierarchy Examples: DNS
Hierarchical name database
Allows delegation of control
  Each organization controls a sub-tree
  May delegate control
Allows scaling of the infrastructure
  A DNS server only needs to know about its sub-domains

## Slide 24: Hierarchy Example: MAC Addresses
Ethernet MAC addresses are globally unique identifiers
  First 3 bytes: manufacturer, allocated by consortium
  Last 3 bytes: allocated by manufacturer

## Slide 25: Indirection
  “Any problem in computer science can be solved with another level of indirection... Except for the problem of too many layers of indirection” David Wheeler
Referencing by name
Goes hand in hand with the layering abstractions
Benefits
  Human convenience
  Makes underlying changes transparent: allows changes underneath
Examples
  Host names versus IP addresses

## Slide 26: Names versus addresses
Names are easier to remember
Addresses can change underneath
Name could map to multiple IP addresses
  E.g. load balancing, or geographically closer server
Multiple names for the same address
Need a way to map one to the other
  DNS hierarchy

## Slide 27: Many Translations
DHCP: Given a MAC Address, assign an IP address
  Uses IP broadcast to find server
ARP: Given an IP address, find Ethernet MAC Addresses
  Uses Link Layer broadcast to find node
DNS: Given a Name, find an IP address
  Uses IP unicast/anycast to well known roots, to bootstrap
  Relies on IP routing infrastructure, DNS hierarchy
DHT: Given a key, find a node
  Uses IP unicast plus efficient flat namespace routing

## Slide 28: Caching
Duplicate data stored elsewhere
  Reduce latency for accessing the data
  Reduce the load on other parts of the system
Often quite effective
  Locality of reference: temporal locality and small set of popular items
Examples:
  Web caching
  DNS caching
  ARP caching
  Learning bridges

## Slide 29: DNS Caching
What is cached?
  Mapping of names to IP addresses
  Lookups that failed
  IP addresses of name servers
Reduces latency
Reduces load on hierarchy
Why is it effective?
  Mostly read database
  Doesn’t change very often
  Popular sites are visited often

## Slide 30: HTTP Caching
What is cached?
  Web objects
Where is it cached?
  Browser, proxy-cache, main memory on server
Reduces latency, load
What contributes to high hit rates?
  Cacheable content (mostly static)
  Sharing the cache among multiple users
  Small amount of popular content

## Slide 31: Randomization
Distributed adaptive algorithms
Risk of synchronization
  Many parties respond to the same conditions in the same way
  May lead to bad aggregate behavior
Randomization can de-synchronize
  Example: Ethernet backoff mechanism
  Example: Random Early Drop
Interesting (extra) read: “The Synchronization of Periodic Routing Messages”,
Sally Floyd and Van Jacobson, Sigcomm 1993

## Slide 32: Soft State
State is stored in nodes by network protocols
  E.g., a mapping, routing entry, cached object
Key issue: how to deal with changes?
Hard state: “valid unless told otherwise”
  “Managed” by originator of state
  Kept consistent, explicit invalidation
Soft state: “valid if fresh”
  Removed by storing node on timeout
  Periodically refreshed as needed
    May need extra cost (on-demand revalidation or check)
  Can be seen as a hint
Soft state reduces complexity
  At the cost of some unpredictability

## Slide 33: Soft state examples
DNS Caching
  TTL
  Can be wrong, check with origin on error
Alternative
  Origin keeps track of copies
  Refresh copies on change in mapping
Cache coherence is hard
  And expensive at scale!
Others
  DHCP lease

## Slide 34: Internet Architecture
A Radical Idea
  Dumb network
  Lowest common denominator (best-effort service)
  No reservations: statistical multiplexing, packets
Amazingly successful
  Architecture has scaled in size…
  Many orders of magnitude difference in bandwidth, latency, jitter, reliability, …

## Slide 35: Growth of the Internet
Source: Miguel Angel Todaro

## Slide 36: Original Design Principles of the Internet
David Clark, 1988 “The Design Philosophy of the DARPA Internet Protocols”
Fundamental Goal:
  Effective technique for multiplexed utilization of existing interconnected networks
Secondary Goals:
  Communication should continue despite loss of nodes
  Multiple types of service
  Variety of networks
  Distributed management of resources
  Cost effective
  Low-effort host attachment
  Resources must be accountable

## Slide 37: But… There are BIG Challenges
Designed in a different environment, with different uses
  Identity / Accountability
  Access model
  Security
  Challenges to openness
Current scale and complexity unimaginable 40 years ago!

## Slide 38: Management
Limited by complexity (“Masters of Complexity”)
SDNs make architectural elements even dumber
Layers for the control plane
Great for single administrative domain, still open question for inter-domain control

## Slide 39: Identity
Leads to
  Spoofing
  Spam
  Denial of service
    Amplification attacks
  Route hijacking
  DNS cache poisoning

## Slide 40: Protocols designed based on trust
That you don’t spoof your address
  MAC spoofing, IP spoofing, email spoofing
That you are who you say you are
  BGP announcements, Websites, DNS servers
That you adhere to the protocol
  Ethernet exponential backoff after a collision
  TCP-friendliness
That protocol specifications are public
  So that others can build interoperable implementations

## Slide 41: Nobody in charge
Traffic traverses many Ass
  Who’s at fault when things go wrong?
  How do you upgrade functionality?
Anyone can add any application
  Whether it is legal, moral, good, well-behaved, etc.
Nobody knows how big the Internet is
Spans many countries
  So no government can be in charge

## Slide 42: Access Models
“On by default”
  Any node can talk to any node (IP, email, web)
  Allows for Denial of Service Attacks!
  Can use a firewall…
    But won’t stop attackers from saturating the paths to you!

## Slide 43: Host versus Data centric
IP is host-to-host protocol
  telnet myhost.mycompany.com
Today
  Users want content, not servers
  Web: many redirections, lots of URLs are not “human readable”
  http://a7.sphotos.ak.fbcdn.net/hphotos-ak-ash1/167898_788691982781_7555_40937029_2012165_n.jpg
  “Lookup” through search engines
  BitTorrent: torrent file describes content, specific peers are irrelevant
Can the architecture support this better?

## Slide 44: Security
Huge challenges
  Public Key Infrastructure
  S-BGP, DNSSEC, IPSec
Spoofing, Poisoning, Phishing
Denial of Service attacks
Cyber-security
  Cyber-war (talk to John Savage)

## Slide 45: Challenges to Openness
Walled Gardens
  E.g., Facebook, Google
  Convenient, easy to use, network effects
  Intrusive data collection
  No control of own data, hard to migrate
  Centralization of trust
  Proprietary protocols
Network Neutrality
  Should all packets be treated equally?
  ISPs are commoditized, want to make money
  Can prioritize own traffic, charge to carry other traffic
  Very hot debate topic

## Slide 46: Other Challenges
Extreme mobility
  Mobile with no fixed attachment point
  How to maintain efficient routing?
Large number of nodes
  Billions of small networked devices (e.g., sensors)
  “Internet of Things”
Sometimes-connected nodes
  Developing regions with intermittent connectivity
Real-time applications
  VoIP, gaming, IPTV

## Slide 47: Future of the Internet
Can we fix these problems
  Security
  Performance
  Upgradability
  Manageability
  … your favorite ailment here …
Without disrupting a critical infrastructure?
Open technical and policy question…

## Slide 48: Thank you!