## Slide 1: CSCI-1680 Switching
Based partly on lecture notes by David Mazières, Phil Levis, John Jannotti
Rodrigo Fonseca

## Slide 2: Administrivia
Homework I out, due next Friday, Feb 18
No class next Tuesday

## Slide 3: Today
Ethernet (cont.)
Link Layer Switching

## Slide 4: Basic Problem
Direct-link networks don’t scale
Solution: use switches to connect network segments

## Slide 5: Switching
Switches must be able to, given a packet, determine the outgoing port
3 ways to do this:
  Datagram Switching
  Virtual Circuit Switching
  Source Routing

## Slide 6: Virtual Circuit Switching
Explicit set-up and tear down phases
  Establishes Virtual Circuit Identifier on each link
  Each switch stores VC table
Subsequent packets follow same path
  Switches map [in-port, in-VCI] : [out-port, out-VCI]
Also called connection-oriented model

## Slide 7: Virtual Circuit Model
Requires one RTT before sending first packet
Connection request contain full destination address, subsequent packets only small VCI
Setup phase allows reservation of resources, such as bandwidth or buffer-space
  Any problems here?
If a link or switch fails, must re-establish whole circuit
Example: ATM
Notes: What is the domain of each VCI?
And the address?

## Slide 8: Datagram Switching
Each packet carries destination address
Switches maintain address-based tables
  Maps [destination address]:[out-port]
Also called connectionless model
Addr | Port
A | 3
B | 0
C | 3
D | 3
E | 2
F | 1
G | 0
H | 0
Switch 2

## Slide 9: Datagram Switching
No delay for connection setup
Source can’t know if network can deliver a packet
Possible to route around failures
Higher overhead per-packet
Potentially larger tables at switches
Notes: Why larger tables?

## Slide 10: Source Routing
Packets carry entire route: ports
Switches need no tables!
  But end hosts must obtain the path information
Variable packet header
Notes: May be loose or strict.
Brittle if there are changes host doesn’t know about.

## Slide 11: Bridges and Extended LANs
LANs have limitations
  E.g. Ethernet < 1024 hosts, < 2500m
Connect two or more LANs with a bridge
  Operates on Ethernet addresses
  Forwards packets from one LAN to the other(s)
Ethernet switch is just a multi-way bridge

## Slide 12: Learning Bridges
Idea: don’t forward a packet where it isn’t needed
  If you know recipient is not on that port
Learn hosts’ locations based on source addresses
  Build a table as you receive packets
Table says when not to forward a packet
  Doesn’t need to be complete for correctness
Notes: Never forward to INCOMING port…
What if hosts move? TIMEOUT
What if no space? Still works

## Slide 13: Bridges
Unicast: forward with filtering
Broadcast: always forward
Multicast: always forward or learn groups
Difference between bridges and repeaters?
  Bridges: same broadcast domain; copy frames
  Repeaters: same broadcast and collision domain; copy signals

## Slide 14: Dealing with Loops
Problem: people may create loops in LAN!
  Accidentally, or to provide redundancy
  Don’t want to forward packets indefinitely

## Slide 15: Spanning Tree
Need to disable ports, so that no loops in network
Like creating a spanning tree in a graph
  View switches and networks as nodes, ports as edges

## Slide 16: Distributed Spanning Tree Algorithm
Every bridge has a unique ID (Ethernet address)
Goal:
  Bridge with the smallest ID is the root
  Each segment has one designated bridge, responsible for forwarding its packets towards the root
    Bridge closest to root is designated bridge
    If there is a tie, bridge with lowest ID wins

## Slide 17: Spanning Tree Protocol
Spanning Tree messages contain:
  ID of bridge sending the message
  ID sender believes to be the root
  Distance (in hops) from sender to root
Bridges remember best config msg on each port
Send message when you think you are the root
Otherwise, forward messages from best known root
  Add one to distance before forwarding
  Don’t forward if you know you aren’t dedicated bridge
In the end, only root is generating messages

## Slide 18: Limitations of Bridges
Scaling
  Spanning tree algorithm doesn’t scale
  Broadcast does not scale
  No way to route around congested links, even if path exists
May violate assumptions
  Could confuse some applications that assume single segment
  Much more likely to drop packets
  Makes latency between nodes non-uniform
  Beware of transparency

## Slide 19: VLANs
Company network, A and B departments
  Broadcast traffic does not scale
  May not want traffic between the two departments
  Topology has to mirror physical locations
  What if employees move between offices?
b1
b2
a1
a2

## Slide 20: VLANs
Solution: Virtual LANs
  Assign switch ports to a VLAN ID (color)
  Isolate traffic: only same color
  Trunk links may belong to multiple VLANs
  Encapsulate packets: add 12-bit VLAN ID
Easy to change, no need to rewire
a2
b2
a1
b1

## Slide 21: Generic Switch Architecture
Goal: deliver packets from input to output ports
Three potential performance concerns:
  Throughput in bytes/second
  Throughput in packets/second
  Latency
Notes: Different if packets are variable size

## Slide 22: Cut through vs. Store and Forward
Two approaches to forwarding a packet
  Receive a full packet, then send to output port
  Start retransmitting as soon as you know output port, before full packet
Cut-through routing can greatly decrease latency
Disadvantage
  Can waste transmission (classic optimistic approach)
  CRC may be bad
  If Ethernet collision, may have to send runt packet on output link

## Slide 23: Buffering
Buffering of packets can happen at input ports, fabric, and/or output ports
Queuing discipline is very important
Consider FIFO + input port buffering
  Only one packet per output port at any time
  If multiple packets arrive for port 2, they may block packets to other ports that are free
  Head-of-line blocking
2
2
1
Port 1
Port 2
Notes: Also allows QoS, Prioritization

## Slide 24: Shared Memory Switch
1st Generation – like a regular PC
  NIC DMAs packet to memory over I/O bus
  CPU examines header, sends to destination NIC
  I/O bus is serious bottleneck
  For small packets, CPU may be limited too
  Typically < 0.5 Gbps

## Slide 25: Shared Bus Switch
2st Generation
  NIC has own processor, cache of forwarding table
  Shared bus, doesn’t have to go to main memory
  Typically limited to bus bandwidth
    (Cisco 5600 has a 32Gbps bus)

## Slide 26: Point to Point Switch
3rd Generation: overcomes single-bus bottleneck
Example: Cross-bar switch
  Any input-output permutation
  Multiple inputs to same output requires trickery
  Cisco 12000 series: 60Gbps
Notes: Layer 3 routers are similar

## Slide 27: Coming Up
Connecting multiple networks: IP and the Network Layer
Remember: no class on Tuesday!