## Slide 1: CSCI-1680 Network Layer: Wrapup
Based partly on lecture notes by Jennifer Rexford, Rob Sherwood, David Mazières, Phil Levis, John Jannotti
Rodrigo Fonseca

## Slide 2: Administrivia
Homework 2 is due Monday
  So we can post solutions before the midterm!
Exam on Tuesday
  All content up to today
  Questions similar to the homework
  Book has some exercises, sample on the course web page

## Slide 3: Today: IP Wrap-up
IP Service models
  Unicast, Broadcast, Anycast, Multicast
ICMP
  Traceroute
  NAT
IPv6
  Tunnels

## Slide 4: Different IP Service Models
Broadcast: send a packet to all nodes in some subnet. “One to all”
  255.255.255.255 : all hosts within a subnet, never forwarded by a router
  “All ones host part”: broadcast address
    Host address | (255.255.255.255 & ~subnet mask)
    E.g.: 128.148.32.143 mask 255.255.255.128
    ~mask = 0.0.0.127 => Bcast = 128.148.32.255
Example use: DHCP
Not present in IPv6
  Use multicast to link local all nodes group

## Slide 5: Anycast
Multiple hosts may share the same IP address
“One to one of many” routing
Example uses: load balancing, nearby servers
  DNS Root Servers (e.g. f.root-servers.net)
  Google Public DNS (8.8.8.8)
  IPv6 6-to-4 Gateway (192.88.99.1)
Notes: dig +norec @F.ROOT-SERVERS.NET HOSTNAME.BIND CHAOS TXT

## Slide 6: Anycast Implementation
Anycast addresses are /32s
At the BGP level
  Multiple ASs can advertise the same prefixes
  Normal BGP rules choose one route
At the Router level
  Router can have multiple entries for the same prefix
  Can choose among many
Each packet can go to a different server
  Best for services that are fine with that (connectionless, stateless)

## Slide 7: Multicast
Send messages to many nodes: “one to many”
Why do that?
  Snowcast, Internet Radio, IPTV
  Stock quote information
  Multi-way chat / video conferencing
  Multi-player games
What’s wrong with sending data to each recipient?
  Link stress
  Have to know address of all destinations
Notes: Wrong: link stress, have to know each recipient

## Slide 8: Multicast Service Model
Receivers join a multicast group G
Senders send packets to address G
Network routes and delivers packets to all members of G
Multicast addresses: class D (start 1110)
224.x.x.x to 229.x.x.x
  28 bits left for group address

## Slide 9: LAN Multicast
Easy on a shared medium
Ethernet multicast address range:
  01:00:57:00:00:00 to 01:00:57:7f:ff:ff
Set low 23 bits of Ethernet address to low bits of IP address
  (Small problem: 28-bit group address -> 23 bits)
  How about on the Internet?

## Slide 10: Use Distribution Trees
Source-specific trees:
  Spanning tree over recipients, rooted at each source
  Best for each source
Shared trees:
  Single spanning tree among all sources and recipients
  Hard to find one shared tree that’s best for many senders
State in routers much larger for source-specific

## Slide 11: Source vs Shared Trees

## Slide 12: Building the Tree: Host to Router
Nodes tell their local routers about groups they want to join
  IGMP, Internet Group Management Protocol (IPv4)
  MLD, Multicast Listener Discovery (IPv6)
Router periodically polls LAN to determine memberships
  Hosts are not required to leave, can stop responding

## Slide 13: Building the Tree across networks
Routers maintain multicast routing tables
  Multicast address -> set of interfaces, or
  <Source, Multicast address> -> set of interfaces
Critical: only include interfaces where there are downstream recipients

## Slide 14: Practical Considerations
Multicast protocols end up being quite complex
Introduce a lot of router state
Turned off on most routers
Mostly used within domains
  In the department: Ganglia monitoring infrastructure
  IPTV on campus
Alternative: do multicast in higher layers

## Slide 15: ICMP

## Slide 16: Internet Control Message Protocol (ICMP)
Echo (ping)
Redirect
Destination unreachable (protocol, port, or host)
TTL exceeded
Checksum failed
Reassembly failed
Can’t fragment
Many ICMP messages include part of packet that triggered them
See http://www.iana.org/assignments/icmp-parameters

## Slide 17: ICMP message format

## Slide 18: Example: Time Exceeded
Code usually 0 (TTL exceeded in transit)
Discussion: traceroute

## Slide 19: Example: Can’t Fragment
Sent if DF=1 and packet length > MTU
What can you use this for?
Path MTU Discovery
  Can do binary search on packet sizes
  But better: base algorithm on most common MTUs
Notes: Path MTU discovery

## Slide 20: Practical Example: Traceroute
Problem: how to determine the path to a given host?
One solution: record route IP option
  Routers add their addresses to the packet as it goes
  Problem: IPv4 option space is only 40 bytes
Another solution: Traceroute
  Uses the TTL field, plus return ICMP Time Exceeded messages, for packets with increasing TTL
  Problems?
Examples

## Slide 21: Network Address Translation (NAT)
Despite CIDR, it’s still difficult to allocate addresses (232 is only 4 billion)
  IPv6 solves this
NAT “hides” entire network behind one address
Hosts are given private addresses
Routers map outgoing packets to a free address/port
Router reverse maps incoming packets
Problems?
Notes: Incoming flows
Shared ports
Breaks assumptions
Eg.: FTP (but FTP is broken)

## Slide 22: IPv6
Main motivation: IPv4 address exhaustion
Initial idea: larger address space
Need new packet format:
  REALLY expensive to upgrade all infrastructure!
  While at it, why don’t we fix a bunch of things in IPv4?
Work started in 1994, basic protocol published in 1998

## Slide 23
Source: potaroo.net

## Slide 24: IPv6 Key Features
128-bit addresses
  Autoconfiguration
Simplifies basic packet format through extension headers
  40-byte base header (fixed)
  Make less common fields optional
Security and Authentication

## Slide 25: IPv6 Address Representation
Groups of 16 bits in hex notation
47cd:1244:3422:0000:0000:fef4:43ea:0001
Two rules:
  Leading 0’s in each 16-bit group can be omitted
  47cd:1244:3422:0:0:fef4:43ea:1
  One contiguous group of 0’s can be compacted
  47cd:1244:3422::fef4:43ea:1

## Slide 26: IPv6 Addresses
Break 128 bits into 64-bit network and 64-bit interface
  Makes autoconfiguration easy: interface part can be derived from Ethernet address, for example
Types of addresses
  All 0’s: unspecified
  000…1: loopback
  ff/8: multicast
  fe8/10: link local unicast
  fec/10: site local unicast
  All else: global unicast

## Slide 27: IPv6 Header

## Slide 28: IPv6 Header Fields
Version: 4 bits, 6
Class: 8 bits, like TOSS in IPv4
Flow: 20 bits, identifies a flow
Length: 16 bits, datagram length
Next Header, 8 bits: …
Hop Limit: 8 bits, like TTL in IPv4
Addresses: 128 bits
No options, no checksum

## Slide 29: Interoperability
RFC 4291
Every IPv4 address has an associated IPv6 address
Simply prefix 32-bit IPv4 address with 96 bits of 0
  E.g., ::128.148.32.2
Two IPv6 endpoints must have IPv6 stacks
Transit network:
  v6 – v6 – v6 : ✔
  v4 – v4 – v4 : ✔
  v4 – v6 – v4 : ✔
  v6 – v4 – v6 : ✗!!

## Slide 30: IP Tunneling
Encapsulate an IP packet inside another IP packet
Makes an end-to-end path look like a single IP hop

## Slide 31: IPv6 in IPv4 Tunneling
Key issues: configuring the tunnels
  Determining addresses
  Determining routes
  Deploying relays to encapsulate/forward/decapsulate
6to4 is a standard to automate this
  Deterministic address generation
  Anycast 192.88.99.1 to find gateway into IPv6 network
  Drawbacks: voluntary relays, requires public endpoint address

## Slide 32: Other uses for tunneling
Virtual Private Networks
Use case: access CS network from the outside
Set up an encrypted TCP connection between your computer and Brown’s OpenVPN server
Configure routes to Brown’s internal addresses to go through this connection
Can connect two remote sites securely

## Slide 33: Extension Headers
Two types: hop-by-hop and end-to-end
Both have a next header byte
Last next header also denotes transport protocol
Destination header: intended for IP endpoint
  Fragment header
  Routing header (loose source routing)
Hop-by-hop headers: processed at each hop
  Jumbogram: packet is up to 232 bytes long!

## Slide 34: Example Next Header Values
0: Hop by hop header
1: ICMPv4
4: IPv4
6:TCP
17: UDP
41: IPv6
43: Routing Header
44: Fragmentation Header
58: ICMPv6

## Slide 35: Fragmentation and MTU
Fragmentation is supported only on end hosts!
Hosts should do MTU discovery
Routers will not fragment: just send ICMP saying packet was too big
Minimum MTU is 1280-bytes
  If some link layer has smaller MTU, must interpose fragmentation reassembly underneath

## Slide 36: Current State
IPv6 Deployment has been slow
Most end hosts have dual stacks today (Windows, Mac OSX, Linux, *BSD, Solaris)
2008 Google study:
  Less than 1% of traffic in any country
Requires all parties to work!
  Servers, Clients, DNS, ISPs, all routers
IPv4 and IPv6 will coexist for a long time

## Slide 37: Next time: Midterm
After that, transport layer and above!
  UDP, TCP, Congestion Control
  Application protocols
  …