## Slide 1: CSCI-1680 Transport Layer I
Based partly on lecture notes by David Mazières, Phil Levis, John Jannotti
Rodrigo Fonseca

## Slide 2: Today
Transport Layer
  UDP
  TCP Intro
    Connection Establishment

## Slide 3: Transport Layer
Transport protocols sit on top of network layer
Problem solved: communication among processes
  Application-level multiplexing (“ports”)
  Error detection, reliability, etc.

## Slide 4: UDP – User Datagram Protocol
Unreliable, unordered datagram service
Adds multiplexing, checksum
End points identified by ports
  Scope is an IP address (interface)
Checksum aids in error detection

## Slide 5: UDP Header

## Slide 6: UDP Checksum
Uses the same algorithm as the IP checksum
  Set Checksum field to 0
  Sum all 16-bit words, adding any carry bits to the LSB
  Flip bits to get checksum (except 0xffff->0xffff)
  To check: sum whole packet, including sum, should get 0xffff
How many errors?
  Catches any 1-bit error
  Not all 2-bit errors
Optional in IPv4: not checked if value is 0

## Slide 7: Pseudo Header
UDP Checksum is computer over pseudo-header prepended to the UDP header
  For IPv4: IP Source, IP Dest, Protocol (=17), plus UDP length
What does this give us?
What is a problem with this?
  Is UDP a layer on top of IP?
0 7 8 15 16 23 24 31
+--------+--------+--------+--------+
| source address |
+--------+--------+--------+--------+
| destination address |
+--------+--------+--------+--------+
| zero |protocol| UDP length |
+--------+--------+--------+--------+

## Slide 8: Next Problem: Reliability
Review: reliability on the link layer
Problem | Mechanism
Acknowledgments + Timeout
Dropped Packets
Duplicate Packets
Sequence Numbers
Packets out of order
Receiver Window
Keeping the pipe full
Sliding Window (Pipelining)
Single link: things were easy… 

## Slide 9: Transport Layer Reliability
Extra difficulties
  Multiple hosts
  Multiple hops
  Multiple potential paths
Need for connection establishment, tear down
  Analogy: dialing a number versus a direct line
Varying RTTs
  Both across connections and during a connection
  Why do they vary? What do they influence?
Notes: RTT influences the potential window size (delay X bandwidth), the values for timeouts.

## Slide 10: Extra Difficulties (cont.)
Out of order packets
  Not only because of drops/retransmissions
  Can get very old packets (up to 120s), must not get confused
Unknown resources at other end
  Must be able to discover receiver buffer: flow control
Unknown resources in the network
  Should not overload the network
  But should use as much as safely possible
  Congestion Control (next class)

## Slide 11: TCP – Transmission Control Protocol
Service model: “reliable, connection oriented, full duplex byte stream”
  Endpoints: <IP Address, Port>
Flow control
  If one end stops reading, writes at other eventually stop/fail
Congestion control
  Keeps sender from overloading the network

## Slide 12: TCP
Specification
  RFC 793 (1981), RFC 1222 (1989, some corrections), RFC 5681 (2009, congestion control), …
Was born coupled with IP, later factored out
  We talked about this, don’t always need everything!
End-to-end protocol
  Minimal assumptions on the network
  All mechanisms run on the end points
Alternative idea:
  Provide reliability, flow control, etc, link-by-link
  Does it work?

## Slide 13: Why not provide (*) on the network layer?
Cost
  These functionalities are not free: don’t burden those who don’t need them
Conflicting
  Timeliness and in-order delivery, for example
Insufficient
  Example: reliability
* may be security, reliability, ordering guarantees, …

## Slide 14: End-to-end argument
Functions placed at lower levels of a system may be redundant or of little value
  They may need to be performed at a higher layer anyway
But they may be justified for performance reasons
  Or just because they provide most of what is needed
  Example: retransmissions
Lesson: weigh the costs and benefits at each layer
  Also: the end also varies from case to case
Notes: Example: Bit-torrent file transfer
Example performance enhancement
o-----o-----o----o 0.1 chance of drop
End-to-end ack: (0.9^4)^2 = 0.43 (~2.3X)
2 Retransmissions per hop:
Failure: fails two retransmissions = ((1-(0.1+0.1*0.9)^2)^4)^2 = 0.74

## Slide 15: TCP Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Port | Destination Port |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Acknowledgment Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Data | |U|A|P|R|S|F| |
| Offset| Reserved |R|C|S|S|Y|I| Window |
| | |G|K|H|T|N|N| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Checksum | Urgent Pointer |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Options | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| data |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 16: Header Fields
Ports: multiplexing
Sequence number
  Correspond to bytes, not packets!
Acknowledgment Number
  Next expected sequence number
Window: willing to receive
  Lets receiver limit SWS (even to 0) for flow control
Data Offset: # of 4 byte header + option bytes
Flags, Checksum, Urgent Pointer

## Slide 17: Header Flags
URG: whether there is urgent data
ACK: ack no. valid (all but first segment)
PSH: push data to the application immediately
RST: reset connection
SYN: synchronize, establishes connection
FIN: close connection

## Slide 18: Establishing a Connection
Three-way handshake
  Two sides agree on respective initial sequence nums
If no one is listening on port: server sends RST
If server is overloaded: ignore SYN
If no SYN-ACK: retry, timeout
Listen, Accept…
Accept returns
Connect

## Slide 19: Connection Termination
FIN bit says no more data to send
  Caused by close or shutdown
  Both sides must send FIN to close a connection
Typical close
FIN
ACK
FIN
ACK
Close
Close
FIN_WAIT_1
CLOSE_WAIT
FIN_WAIT_2
LAST_ACK
TIME_WAIT
CLOSED
CLOSED
…
2MSL

## Slide 20: Summary of TCP States
Passive close:
Can still send!
Active close:
Can still receive
Connection Establishment
Unsynchronized
Synchronized

## Slide 21: TIME_WAIT
Why do you have to wait for 2MSL in TIME_WAIT?
  What if last ack is severely delayed, AND
  Same port pair is immediately reused for a new connection?
Solution: active closer goes into TIME_WAIT
  Waits for 2MSL (Maximum Segment Lifetime)
Can be problematic for active servers
  OS has too many sockets in TIME_WAIT, can accept less connections
    Hack: send RST and delete socket, SO_LINGER = 0
  OS won’t let you re-start server because port in use
    SO_REUSEADDR lets you rebind

## Slide 22: Next class
Sending data over TCP