## Slide 1: CSCI-1680 Link Layer Reliability
Based partly on lecture notes by David Mazières, Phil Levis, John Jannotti
Rodrigo Fonseca

## Slide 2
Last time
  Physical layer: encoding, modulation
  Link layer framing
Today
  Getting frames across: reliability, performance

## Slide 3: Sending Frames Across
Transmission Delay
Propagation Delay
Latency
Notes: How long does it take to send a frame across?

## Slide 4: Sending Frames Across
Throughput: bits / s
…
…
Notes: How fast can we receive bytes?

## Slide 5: Which matters most, bandwidth or delay?
How much data can we send during one RTT?
E.g., send request, receive file
Time
Request
Response
For small transfers, latency more important, for bulk, throughput more important

## Slide 6: Performance Metrics
Throughput - Number of bits received/unit of time
  e.g. 10Mbps
Goodput - Useful bits received per unit of time
Latency – How long for message to cross network
  Process + Queue + Transmit + Propagation
Jitter – Variation in latency

## Slide 7: Latency
Processing
  Per message, small, limits throughput
  e.g. or 120μs/pkt
Queue
  Highly variable, offered load vs outgoing b/w
Transmission
  Size/Bandwidth
Propagation
  Distance/Speed of Light

## Slide 8: Reliable Delivery
Several sources of errors in transmission
Error detection can discard bad frames
Problem: if bad packets are lost, how can we ensure reliable delivery?
  Exactly-once semantics = at least once + at most once

## Slide 9: At Least Once Semantics
How can the sender know packet arrived at least once?
  Acknowledgments + Timeout
Stop and Wait Protocol
  S: Send packet, wait
  R: Receive packet, send ACK
  S: Receive ACK, send next packet
  S: No ACK, timeout and retransmit

## Slide 11
Notes: Can the sender differentiate between (b) and (c) ?
In (c) and (d), DOES THE RECEIVER KNOW WHETHER THE FRAME IS A NEW FRAME OR A RETRANSMISSION?

## Slide 12: Stop and Wait Problems
Duplicate data
Duplicate acks
Slow (channel idle most of the time!)
May be difficult to set the timeout value

## Slide 13: Duplicate data: adding sequence numbers

## Slide 14: At Most Once Semantics
How to avoid duplicates?
  Uniquely identify each packet
  Have receiver and sender remember
Stop and Wait: add 1 bit to the header
  Why is it enough?

## Slide 15: Going faster: sliding window protocol
Still have the problem of keeping pipe full
  Generalize approach with > 1-bit counter
  Allow multiple outstanding (unACKed) frames
  Upper bound on unACKed frames, called window

## Slide 16: How big should the window be?
How many bytes can we transmit in one RTT?
  BW B/s x RTT s => “Bandwidth-Delay Product”

## Slide 17: Maximizing Throughput
Can view network as a pipe
  For full utilization want bytes in flight ≥ bandwidth × delay
  But don’t want to overload the network (future lectures)
What if protocol doesn’t involve bulk transfer?
  Get throughput through concurrency – service multiple clients simultaneously

## Slide 18: Sliding Window Sender
Assign sequence number (SeqNum) to each frame
Maintain three state variables
  send window size (SWS)
  last acknowledgment received (LAR)
  last frame sent (LFS)
Maintain invariant: LFS – LAR ≤ SWS
Advance LAR when ACK arrives
Buffer up to SWS frames

## Slide 19: Sliding Window Receiver
Maintain three state variables:
  receive window size (RWS)
  largest acceptable frame (LAF)
  last frame received (LFR)
Maintain invariant: LAF – LFR ≤ RWS
Frame SeqNum arrives:
  if LFR < SeqNum ≤ LAF, accept
  if SeqNum ≤ LFR or SeqNum > LAF, discard
Send cumulative ACKs
Notes: How to set SWS? -> You want to “fill the pipe”, so look at the BW delay product, or how many frames you can send in one RTT
How to set RWS? -> A RWS > 1 allows for more efficiency, as you can accept packets out of order.
What is this accomplishing? Reliability, Ordering, Flow Control

## Slide 20: Tuning Send Window
How big should SWS be?
  “Fill the pipe”
How big should RWS be?
  1 ≤ RWS ≤ SWS
How many distinct sequence numbers needed?

## Slide 21: Example
SWS = RWS = 5. Are 6 seq #s enough?
Sender sends 0,1,2,3,4
All acks are lost
Sender sends 0,1,2,3,4 again
…
What are the possible views of the sender and receiver?
Notes: We would need to make sure that all packets the sender can send in this case can be distinguished!
If the sender advances the whole window, there can’t be any repeated sequence numbers.

## Slide 22: Tuning Send Window
How big should SWS be?
  “Fill the pipe”
How big should RWS be?
  1 ≤ RWS ≤ SWS
How many distinct sequence numbers needed?
  SWS can’t be more than half of the space of valid seq#s.

## Slide 23: Summary
Want exactly once
  At least once: acks + timeouts + retransmissions
  At most once: sequence numbers
Want efficiency
  Sliding window

## Slide 25: Error Detection
Idea: have some codes be invalid
  Must add bits to catch errors in packet
Sometimes can also correct errors
  If enough redundancy
  Might have to retransmit
Used in multiple layers
Three examples today:
  Parity
  Internet Checksum
  CRC

## Slide 26: Simplest Schemes
Repeat frame n times
  Can we detect errors?
  Can we correct errors?
    Voting
  Problem: high redundancy : n
Example: send each bit 3 times
  Valid codes: 000 111
  Invalid codes : 001 010 011 100 101 110
  Corrections : 0 0 1 0 1 1

## Slide 27: Parity
Add a parity bit to the end of a word
Example with 2 bits:
  Valid: 000 011 011 110
  Invalid: 001 010 010 111
  Can we correct?
Can detect odd number of bit errors
  No correction
Notes: Cannot correct because each invalid code is the same distance from 3 valid codes!

## Slide 28: In general
Hamming distance: number of bits that are different
  E.g.: HD (00001010, 01000110) = 3
If min HD between valid codewords is d:
  Can detect d-1 bit error
  Can correct ⌊(d-1)/2⌋ bit errors
What is d for parity and 3-voting?
Notes: Parity: d=2
3-Voting: d=3

## Slide 29: 2-D Parity
Add 1 parity bit for each 7 bits
Add 1 parity bit for each bit position across the frame)
  Can correct single-bit errors
  Can detect 2- and 3-bit errors, most 4-bit errors
Find a 4-bit error that can’t be corrected
Notes: Any corners of a square can’t be corrected

## Slide 30: IP Checksum
Fixed-length code
  n-bit code should capture all but 2-n fraction of errors
    Why?
  Trick is to make sure that includes all common errors
IP Checksum is an example
  1’s complement of 1’s complement sum of every 2 bytes
uint16 cksum(uint16 *buf, int count) {
uint32 sum = 0;
while (count--)
if ((sum += *buf++) & 0xffff0000) // carry
sum = (sum & 0xffff) + 1;
return ~(sum & 0xffff);
}
Checking
  Do the sum again, including the checksum. If correct, the sum should be all 1’s (This is super fast to check)
Notes: Each value maps to one code value. If there are 2^n code values, a fraction of 1/(2^n) values maps to each code value.
Take the values that map to the same code value. If you have an error that goes from one of these to the other, without changing the code value, you won’t detect an error. All others should be detected.

## Slide 31: How good is it?
16 bits not very long: misses how many errors?
  1 in 216, or 1 in 64K errors
Checksum does catch all 1-bit errors
But not all 2-bit errors
  E.g., increment word ending in 0, decrement one ending in 1
Checksum also optional in UDP
  All 0s means no checksums calculated
  If checksum word gets wiped to 0 as part of error, bad news

## Slide 32: From rfc791 (IP)
“This is a simple to compute checksum and experimental evidence indicates it is adequate, but it is provisional and may be replaced by a CRC procedure, depending on further experience.”

## Slide 33: CRC – Error Detection with Polynomials
Goal: maximize protection, minimize bits
Consider message to be a polynomial in Z2[x]
  Each bit is one coefficient
  E.g., message 10101001 -> m(x) = x7 + x5+ x3 + 1
Can reduce one polynomial modulo another
  Let n(x) = m(x)x3. Let C(x) = x3 + x2 + 1.
  n(x) “mod” C(x) : r(x)
  Find q(x) and r(x) s.t. n(x) = q(x)C(x) + r(x) and degree of r(x) < degree of C(x)
  Analogous to taking 11 mod 5 = 1

## Slide 34: Polynomial Division Example
Just long division, but addition/subtraction is XOR

## Slide 35: CRC
Select a divisor polynomial C(x), degree k
  C(x) should be irreducible – not expressible as a product of two lower-degree polynomials in Z2[x]
Add k bits to message
  Let n(x) = m(x)xk (add k 0’s to m)
  Compute r(x) = n(x) mod C(x)
  Compute n'(x) = n(x) – r(x) (will be divisible by C(x)) (subtraction is XOR, just set k lowest bits to r(x)!)
Checking CRC is easy
  Reduce message by C(x), make sure remainder is 0
Notes: Irreducible analogous to prime

## Slide 36: Why is this good?
Suppose you send m(x), recipient gets m’(x)
  E(x) = m’(x) – m(x) (all the incorrect bits)
  If CRC passes, C(x) divides m’(x)
  Therefore, C(x) must divide E(x)
Choose C(x) that doesn’t divide any common errors!
  All single-bit errors caught if xk, x0 coefficients in C(x) are 1
  All 2-bit errors caught if at least 3 terms in C(x)
  Any odd number of errors if last two terms (x + 1)
  Any error burst less than length k caught

## Slide 37: Common CRC Polynomials
Polynomials not trivial to find
  Some studies used (almost) exhaustive search
CRC-8: x8 + x2 + x1 + 1
CRC-16: x16 + x15 + x2 + 1
CRC-32: x32 + x26 + x23 + x22 + x16 + x12 + x11 + x10 + x8 + x7 + x5 + x4 + x2 + x1 + 1
CRC easily computable in hardware
Notes: Not tri

## Slide 38: An alternative for reliability
Erasure coding
  Assume you can detect errors
  Code is designed to tolerate entire missing frames
    Collisions, noise, drops because of bit errors
  Forward error correction
Examples: Reed-Solomon codes, LT Codes, Raptor Codes
Property:
  From K source frames, produce B > K encoded frames
  Receiver can reconstruct source with any K’ frames, with K’ slightly larger than K
  Some codes can make B as large as needed, on the fly

## Slide 39: LT Codes
Luby Transform Codes
  Michael Luby, circa 1998
Encoder: repeat B times
  Pick a degree d
  Randomly select d source blocks. Encoded block tn= XOR or selected blocks

## Slide 40: LT Decoder
Find an encoded block tn with d=1
Set sn = tn
For all other blocks tn’ that include sn ,
set tn’=tn’ XOR sn
Delete sn from all encoding lists
Finish if
  You decode all source blocks, or
  You run out out blocks of degree 1

## Slide 41: Next class
Link Layer II
  Ethernet: dominant link layer technology
    Framing, MAC, Addressing
  Switching