## Slide 1: CSCI-1680 Network Layer: Inter-domain Routing
Based partly on lecture notes by Rob Sherwood, David Mazières, Phil Levis, John Jannotti
Rodrigo Fonseca

## Slide 2: Today
Last time: Intra-Domain Routing (IGP)
  RIP distance vector
  OSPF link state
Inter-Domain Routing (EGP)
  Border Gateway Protocol
  Path-vector routing protocol

## Slide 3: Why Inter vs. Intra
Why not just use OSPF everywhere?
  E.g., hierarchies of OSPF areas?
  Hint: scaling is not the only limitation
BGP is a policy control and information hiding protocol
  intra == trusted, inter == untrusted
  Different policies by different ASs
  Different costs by different ASs

## Slide 4: Types of ASs
Local Traffic – source or destination in local AS
Transit Traffic – passes through an AS
Stub AS
  Connects to only a single other AS
Multihomed AS
  Connects to multiple ASs
  Carries no transit traffic
Transit AS
  Connects to multiple ASs and carries transit traffic

## Slide 5: AS Relationships
How to prevent X from forwarding transit between B and C?
How to avoid transit between CBA ?
  B: BAZ -> X (“B advertises BAZ to X”)
  B: BAZ -> C ? (=> Y: CBAZ and Y:CAZ)
B
A
C
X
Y
Z
Example from Kurose and Ross, 5th Ed
Notes: X sends to Y over C, sends to Z over BA. What happens if B sends a packet to X with destination at Y?
X should never advertise any paths to B that include C.
B advertises BAZ to X
B should not advertise BAZ to C

## Slide 6: Choice of Routing Algorithm
Constraints
  Scaling
  Autonomy (policy and privacy)
Link-state?
  Requires sharing of complete information
  Information exchange does not scale
  Can’t express policy
Distance Vector?
  Scales and retains privacy
  Can’t implement policy
  Can’t avoid loops if shortest path not taken
  Count-to-infinity

## Slide 7: Path Vector Protocol
Distance vector algorithm with extra information
  For each route, store the complete path (ASs)
  No extra computation, just extra storage (and traffic)
Advantages
  Can make policy choices based on set of ASs in path
  Can easily avoid loops

## Slide 8: BGP - High Level
Single EGP protocol in use today
Abstract each AS to a single node
Destinations are CIDR prefixes
Exchange prefix reachability with neighbors
  E.g., “I can reach prefix 128.148.0.0/16 through ASes 44444 3356 14325 11078”
  May choose to not advertise some paths to some neighbors
Select a single path by routing policy
Critical: learn many paths, propagate one
  Add your ASN to advertised path

## Slide 9: BGP Implications
Explicit AS Path == Loop free
  Except under churn, IGP/EGP mismatch
Not all ASs know all paths
Reachability not guaranteed
  Decentralized combination of policies
AS abstraction -> loss of efficiency
Scaling
  55K ASs
  685K+ prefixes
  ASs with one prefix: 21292
  Most prefixes by one AS: 5551 (AS4538 ERX-CERNET-BKB - China Education and Research Network Center)
Source: cidr-report 17Oct2017

## Slide 10: Why study BGP?
Critical protocol: makes the Internet run
  Only widely deployed EGP
Active area of problems!
  Efficiency
  Cogent vs. Level3: Internet Partition
  Spammers use prefix hijacking
  Pakistan accidentally took down YouTube
  Egypt disconnected for 5 days

## Slide 11: BGP Example

## Slide 12: BGP Example

## Slide 13: BGP Example

## Slide 14: BGP Example

## Slide 15: BGP Example

## Slide 16: BGP Protocol Details
Separate roles of speakers and gateways
  Speakers talk BGP with other ASs
  Gateways are routes that border other Ass
  Can have more gateways than speakers
  Speakers know how to reach gateways
Speakers connect over TCP on port 179
  Bidirectional exchange over long-lived connection

## Slide 17: BGP Table Growth
Source: bgp.potaroo.net

## Slide 18: BGP Table Growth for v6
Source: bgp.potaroo.net

## Slide 19: Integrating EGP and IGP
Stub ASs
  Border router clear choice for default route
  Inject into IGP: “any unknown route to border router”
Inject specific prefixes in IGP
  E.g., Provider injects routes to customer prefix
Backbone networks
  Too many prefixes for IGP
  Run internal version of BGP, iBGP
  All routers learn mappings: Prefix -> Border Router
  Use IGP to learn: Border Router -> Next Hop

## Slide 20: iBGP

## Slide 21: iBGP

## Slide 22: BGP Messages
Base protocol has four message types
  OPEN – Initialize connection. Identifies peers and must be first message in each direction
  UPDATE – Announce routing changes (most important message)
  NOTIFICATION – Announce error when closing connection
  KEEPALIVE – Make sure peer is alive
Extensions can define more message types
  E.g., ROUTE-REFRESH [RFC 2918]

## Slide 23: Anatomy of an UPDATE
Withdrawn routes: list of withdrawn IP prefixes
Network Layer Reachability Information (NLRI)
  List of prefixes to which path attributes apply
Path attributes
  ORIGIN, AS_PATH, NEXT_HOP, MULTI-EXIT-DISC, LOCAL_PREF, ATOMIC_AGGREGATE, AGGREGATOR, …
  Each attribute has 1-byte type, 1-byte flags, length, content
  Can introduce new types of path attribute – e.g., AS4_PATH for 32-bit AS numbers

## Slide 24: Example
NLRI: 128.148.0.0/16
AS Path: ASN 44444 3356 14325 11078
Next Hop IP: same as in RIPv2
Knobs for traffic engineering:
  Metric, weight, LocalPath, MED, Communities
  Lots of voodoo
Notes: MED is multiple exit discriminator
Communities may limit the scope of advertisements

## Slide 25: BGP State
BGP speaker conceptually maintains 3 sets of state
Adj-RIB-In
  “Adjacent Routing Information Base, Incoming”
  Unprocessed routes learned from other BGP speakers
Loc-RIB
  Contains routes from Adj-RIB-In selected by policy
  First hop of route must be reachable by IGP or static route
Adj-RIB-Out
  Subset of Loc-RIB to be advertised to peer speakers

## Slide 26: Demo
Route views project: http://www.routeviews.org
  telnet route-views.linx.routeviews.org
  show ip bgp 128.148.0.0/16 longer-prefixes
All paths are learned internally (iBGP)
Not a production device

## Slide 27: Next class
BGP Policy Routing and Security